## Slide 1: Design of Silicon Photonic Bragg Grating Devices with Lumerical Vancouver, BC, Canada 10 January 2020
Mustafa Hammood,
The University of British Columbia, Vancouver

## Slide 2: Outline
  Bragg gratings:
    Theoretical approach: Transfer-Matrix Method (TMM)
    Theoretical approach: Coupled-mode theory (CMT)
      Coupling coefficient (Kappa)
    Simulation: Lumerical EME
    Simulation: Lumerical 3D/2D FDTD
    Simulation + Theory: Lumerical FDTD Band-structure
  Contra-directional couplers:
    Theoretical approach
    Simulation: Lumerical EME
    Simulation + Theory: Coupled-mode theory + Transfer-Matrix Method
    Compact model generation and full-simulation flow
  Examples:
    Bragg grating: corrugation strength sweep

## Slide 3: Bragg Gratings: Transfer-Matrix Method

## Slide 4: Bragg Gratings: Transfer-Matrix Method
  Available: https://github.com/mustafacc/SiEPIC_Photonics_Package/blob/master/SiEPIC_Photonics_Package/solvers_simulators/bragg_tmm/bragg_tmm.py
  Handy tool to quickly model phase-shifted Bragg gratings
  Inputs:
    Waveguides compact models (effective indices fits, n(λ) )
    Period
    Number of corrugations
    Perturbation size
  Advantages:
    Quick and simple
    Does not scale up with the length of the device
    Can simulate complex device profiles (apodized, chirped, etc.)
  Disadvantages:
    Must have data to fit the coupling coefficient profile vs perturbation size!

## Slide 5: Bragg Gratings: Transfer-Matrix Method
  Sample spectra:

## Slide 6: Bragg Gratings: EME
  Uses the EME method:
    Explained: https://apps.lumerical.com/pic_passive_bragg_full_device_simulation_with_eme.html
    Video tutorial: https://www.lumerical.com/support/video/waveguide-bragg-gratings-res.html
  Advantages:
    Does not need information other than the physical geometry of the device
    Relatively fast simulation time compared to FDTD
  Disadvantages:
    Simulation time scales up with the complexity of the profile
    Simulation time scales up with the number of simulation modes required to simulate the device
    Less accurate than FDTD simulations

## Slide 7: Bragg Gratings: EME
  Run sample code MAIN_EME.lsf
  Input parameters:
    Device physical parameters

## Slide 8: Bragg Gratings: EME

## Slide 9: Bragg Gratings: EME
  EME simulations can be used to quickly perform parametric studies to understand the effects of specific parameters, i.e. the effects of changing the waveguide’s sidewall angle:
  Run applications -> dw_sweep -> MAIN_dw_sweep.lsf

## Slide 10: Bragg Gratings: 3D/2D FDTD
  Uses FDTD solver:
    Simulating the full device length either in 2D FDTD or 3D FDTD
  Advantages:
    Accurate, if the simulation mesh and time were sufficiently large…
    Can be used to simulated complex apodization provide.
  Disadvantages:
    Very lengthy simulation time!

## Slide 11: Bragg Gratings: 3D/2D FDTD
  Open FDTD project MAIN_FDTD.fsp and Run sample code MAIN_FDTD.lsf
  Input parameters:
    Device physical parameters
    Simulation parameters
  You can create an S-parameters sweep as well.
    You can use ports symmetry.
* There are rarely times you need to actually use 3D FDTD to simulate an entire length of a Bragg grating device. The example is added here for illustrating the inefficiency of the method relative to other methods.

## Slide 12: Bragg Gratings: FDTD Bloch Boundary
  Uses FDTD solver:
    Simulating one unit cell of a grating over an infinite length.
  Advantages:
    Relatively fast simulation with the most accurate results.
    Can be used to perform various parametric sweeps.
  Disadvantages:
    Cannot simulate the output spectra of advanced apodized devices (directly).
    Does not show the output spectra of the device

## Slide 13: Bragg Gratings: FDTD Bloch Boundary
  Two examples provided under ‘Bandstructure’
    Script-based: run ‘MAIN_Bandstructure.lsf’ using FDTD script window with simulation and physical parameters. This is a “GUI”-less approach that will setup the simulation for you.
    Project-based: open “Bragg_bandstructure.fsp’ using FDTD and configure the simulation settings under “model” and physical settings under “Bragg” objects.
      Sample parametric sweeps were setup in this project as an example.